## Slide 1
DIGITAL LOCKING SYSTEM WITH UNAUTHORIZED ACCESS ALERT
Presented By :23ECE381C10
Group Members:
Chittesh S(CB.EN.U4ECE23212)
Sricharan R P(CB.EN.U4ECE23246)
Sujith Krishna P G(CB.EN.U4ECE23249)
23ECE381 Open Laboratory I

## Slide 2
OVERVIEW
  Objectives
  Block Diagram
  Circuit Diagram
  Design
  Analysis
  References

## Slide 3
OBJECTIVES
  To develop a digital locking system using only digital logic circuits
  To integrate a keypad for password entry
  To make the saved password customizable
  To provide visual and audio indication for password verification
  To test logic sequence, reset, and correct code detection mechanisms.

## Slide 4
BLOCK DIAGRAM

## Slide 5
CIRCUIT DIAGRAM

## Slide 6
DESIGN
Procedure:
  When a button is pressed, it provides an active-low signal to a priority encoder. To work with active-high logic, NOT gates are placed at both the input and output of the encoder.
  An Enter button with a demultiplexer switches between password set mode and unlock mode, storing the 4-bit binary input in shift registers
  D flip-flop, configured as a counter, works with the demultiplexer to automatically route each entered digit to the next shift register in sequence.

## Slide 7
DESIGN
Procedure:
  The core authentication is handled by 4-bit magnitude comparators. These ICs compare the binary value from the "user input" registers against the "saved password" registers (B inputs)
  Correct Password: A 4-input AND gate is connected to the A=B outputs of all comparators. If all digits match, this gate's output goes HIGH, which turns on the green led
  Incorrect Password: An 8-input OR gate is connected to all A>B and A<B outputs of the comparators. If any digit is mismatched, this gate's output goes HIGH, which activates the red LED and the buzzer.

## Slide 8
DESIGN
Choice of Components
  Push Buttons
  74147 – 10-to-4 Line Encoder
  74194 – 4-Bit Bidirectional Shift Register
  4013 – D-Type Flip-Flop
  4555 – Dual 1-to-4 Decoder/Demultiplexer
  AND Gates
  OR Gates
  NOT Gates
  7485 – 4-Bit Magnitude Comparator
  Green LED
  Red LED

## Slide 9
ANALYSIS
Keypad & Encoder: User presses a button (e.g., ‘8’) → Encoder outputs 4-bit binary 1000.
Reset Function:
  Reset button clears user input shift registers → system ready for retry.
Comparator Stage:
  A inputs = User-entered digits.
  B inputs = Saved password digits.
If match → A=B = HIGH;
If mismatch → A<B or A>B = HIGH.
Final Logic Output:
Correct Password: All A=B HIGH → 4-input AND → Green LED
Incorrect Password: Any mismatch → 8-input OR → Red LED

## Slide 10
REFERENCES
[1] S. H. Kumar, Electronics Project, vol. 15: Programmable Number Lock.
[2] “GSM Based Digital Door Lock Security System,” in 2015 IEEE International Conference on Power, Instrumentation, Control and Computing (PICC), 2015.
[3] “A Practical Digital Door Lock for Smart Home,” in 2018 IEEE International Conference on Consumer Electronics (ICCE), 2018.
[4] “The Design and Construction of a 2-Digit Electronic Lock System Using Simple Circuit Elements and Digital Electronic Logic Gates,” ResearchGate, Mar. 15, 2017.
[5] “Simple Combination Lock,” All About Circuits. [Online]. Available: https://www.allaboutcircuits.com/textbook/experiments/chpt-7/simple-combination-lock/.
[6] “Electronic Code Lock System Using IC,” Instructables. [Online]. Available: https://www.instructables.com/Electronic-Code-Lock-System-Using-IC/.
[7] “Digital Code Lock Circuit Without Microcontroller,” Gadgetronicx. [Online]. Available: https://www.gadgetronicx.com/digital-code-lock-circuit-without-microcontroller/.

## Slide 11
THANK YOU